## Slide 1
In the PUMA manipulator shown in the figure below, assign frames according to the DH method. Then derive the DH table and simulate the robot in MATLAB.

## Slide 2: Standard (distal) DH convention
an: distance along xn, zn-1->zn
αn: rotation about xn, zn-1->zn
dn: distance along zn-1, xn-1 -> xn
θn: rotation about zn-1, xn-1 -> xn
n | an | an | dn | n
1 |  |  |  | 
Zn axis of n+1th joint
Xn is normal to both Zn-1 and Zn from n-1 to n

## Slide 3
Frames by the standard (distal) DH convention
n | an | an | dn | θn
1 | 0 | -90o | L1 | θ1
2 | L2 | 0 | d2 | θ2
3 | L3 | 0 | 0 | θ3
z1
z2
z3
z0
x1
x0
x2
x3
d2
Standard DH table
Example of simulation in MATLAB
using Peter Corke’s robotic toolbox

## Slide 4: Example code
clear
clc
L1 = 1 ;
L2 = 0.7 ;
L3 = 0.7 ;
d2 = 0.5 ;
J1 = Link('d', L1,'a',0,'alpha',-pi/2); %
J2 = Link('d', d2,'a',L2,'alpha',0); %
J3 = Link('d', 0,'a',L3,'alpha',0); %
% Define the serially connected robot:
PUMA = SerialLink([J1 J2 J3], 'name', 'PUMA')
%You can now "teach" the robot by changing q1 q2 q3 and see the x,y,z and
%Roll-Pitch-Yaw
PUMA.plot([-pi/3,pi/6,pi/6])
PUMA.teach
xlabel('x (m)')
ylabel('y (m)')
zlabel('z (m)')